Numbers Representation
Operating Systems I
Victor Yacovlev (Viktor Iakovlev)

---
The Binary System
01010101
Result: = 0*27 + 1*26 + 0*25 + 0*24 + 0*23 + 1*22 + 0*21 + 1*20
0	- Voltage is less then 0-thereshold (usually 0.7V for most chips)
1	- Voltage is greater then 1-thereshold (usually 2.0V for most chips)
undefined	- Voltage between theresholds

---
Integer Types
- The Byte – is the smallest data amount able to address
- The Bit – 0 or 1. Individual bits are not accessible directly from memory
- The Word – several Bytes processor accesses at once

---
Bits Manipulation
- Shift Left, Right: << >>
- Bitwise operations: &, |, ^, ~
- Use & mask to extract bit at specific positions
- Use | operations to add some bits into ‘set’

---
Byte Order
00000000 11111111
- 255 in case of red byte is low order
- 65’280 in case of blue byte is low order
Which byte order is correct?
Both

---
Byte Order
- From High to Low (like people writes) – Big Endian
  - default mode for PowerPC, MIPS, SPARC
  - standard for network data exchange
- From Low to High (like arabic letters) – Little Endian
  - all x86 processors family and default mode for ARM

---
Signed v.s. UnSigned
Unsigned	Binary	Signed	Two’s Complement
0	0000	0	0
1	0001	1	1
2	0010	2	2
3	0011	3	3
4	0100	4	4
5	0101	5	5
6	0110	6	6
7	0111	7	7
8	1000	-0	-8
9	1001	-1	-7
10	1010	-2	-6
11	1011	-3	-5
12	1100	-4	-4
13	1101	-5	-3
14	1110	-6	-2
15	1111	-7	-1

---
Signed v.s. UnSigned
Unsigned	Binary	Signed	Two’s Complement
0	0000	0	0
1	0001	1	1
2	0010	2	2
3	0011	3	3
4	0100	4	4
5	0101	5	5
6	0110	6	6
7	0111	7	7
8	1000	-0	-8
9	1001	-1	-7
10	1010	-2	-6
11	1011	-3	-5
12	1100	-4	-4
13	1101	-5	-3
14	1110	-6	-2
15	1111	-7	-1

---
Overflow
X + Y = Z + C
When X, Y, Z are fixed-size numbers
C > 0 – means overflow
C=0 ←→ Z>=X and Z>=Y
But… only when X>=0 and Y>=0

---
Overflow
- There is no standard function in C and C++ to check overflows
- But most processors support overflow detection
- Use GCC builtins (non standard functions)

---
The Real Values
- Fixed-Point
  - several meaningful bytes for fractional part
  - often used for ‘Currency’ type in applications
- Floating-Point
  - arbitary fractional part
  - less precise
  - more complex to implement

---
The Real Types
- Float – 32 bit, values about +- 1037
- Double – 64 bit, values about +- 10307

---
IEEE 754 Representation
Single-Precision (type float); B = 127
S (1 bit)	E (8 bits)	M (23 bits)
Double-Precision (type double); 1023
S (1 bit)	E (11 bits)	M (52 bits)
Value = (-1)S ∙ 2E-B ∙ (1 + M / (223or52 -1) )

---
Special Values
- Zeroes: M=0, E=0, S – any
- Infinity: M=0, E=maximum, S – any
- Not-a-Number: M<>0, E=maximum, S – any
- Denormalized (not all processors support):
  E=0, M – any, S – any

---
Denormalized Values
Single-Precision (type float); B = 127
S (1 bit)	E (8 bits)	M (23 bits)
Double-Precision (type double); 1023
S (1 bit)	E (11 bits)	M (52 bits)
Regular Values (when E>0):
Value = (-1)S ∙ 2E-B ∙ (1 + M / (223or52 -1) )
Denormalized Values (when E=0):
Value = (-1)S ∙ M / (223or52 -1)